## Slide 1
CURBRISK
Find the puddle before
it floods the basement.
Street-level drainage risk scoring from LiDAR + pavement + 311.
Cyvl Hackathon 2026 · Somerville, MA demo footprint

## Slide 2
THE PROBLEM
Cities and insurers price flood risk with the wrong map.
FOR INSURERS
FEMA zones stop at the parcel.
Two homes on the same block — one at a low point with a
failing catch basin, one on a crest — pay the same premium.
Underwriters have no measured, coordinate-level signal
for which addresses pond. Cat modelers (RMS, Verisk)
lack sub-zone drainage granularity.
FOR CITIES
Budgets follow complaints, not water.
Streets get repaved over unresolved drainage and fail
again in 18 months. The loudest neighborhood wins
the budget; the most hydraulically stressed one doesn't.
Climate change compresses storms into shorter bursts —
1970s-era basins now see 2020s-era loads.
CurbRisk · Cyvl Hackathon 2026
2 / 7

## Slide 3
THE SOLUTION
CurbRisk: a measured, address-level flood score.
LiDAR
53.5M points
road-surface DEM
Hydrology
low-point detection,
catchment + 2-in ponding
Score
topo 40 / PCI 30 /
basin 20 / 311 10
Deliver
APS cross-section
+ address API
WHAT COMES OUT
A 0–100 CurbRisk score per street segment, a browser-viewable 3D cross-section
of every flagged low point, and an API an underwriter queries by address in < 10 s.
Demo footprint: 1 Somerville tile · 5,080 pavement sections · 381 catch basins · 145 flooding 311s
CurbRisk · Cyvl Hackathon 2026
3 / 7

## Slide 4
WHY IT WINS
Four data layers nobody else has integrated.
Measured terrain, not assumed
Mobile LiDAR captures the 2-inch crown differential that 1-meter DEMs miss. We see where water actually goes.
Pavement + drainage in one model
Cyvl PCI scores tell us where the road is already weak; terrain tells us where water lands on it. The intersection is where potholes reappear.
311 as ground truth
144 Somerville flooding reports validate every modeled low point. If complaints cluster on our high-risk segments, the model is right.
Autodesk-ready, browser-viewable
Every flagged low point exports as an APS cross-section an underwriter opens in a browser — and a civil engineer opens in Civil 3D.
The moat: nobody else holds measured LiDAR + pavement condition + drainage hydrology + Autodesk delivery in one stack.
CurbRisk · Cyvl Hackathon 2026
4 / 7

## Slide 5
BUYERS & VALUE
Two markets, one engine.
PRIMARY · INSURANCE & RISK
Address-level flood pricing
· Underwriters: per-query API at point of sale
· Actuaries: portfolio loss exposure below the FEMA zone
· Cat modelers (RMS, Verisk): bulk dataset license
Differentiates premiums between the crest house and
the low-point house on the same block.
SECONDARY · MUNICIPAL DPW
Defensible capital prioritization
· Stop repaving over unresolved drainage
· Auto-generate MS4 / NPDES gap analysis
· Hand civil engineers a Civil 3D starting model
· Move to the front of FEMA BRIC / EPA CWSRF queues
Replaces complaint-driven politics with a ranked, auditable list.
CurbRisk · Cyvl Hackathon 2026
5 / 7

## Slide 6
LIVE DEMO
Address in. Drainage risk out. Under 10 seconds.
JUDGE ENTERS
93 Highland Ave
Somerville, MA
CURBRISK API
Geocode → segment lookup
SQLite score cache hit
CURBRISK SCORE
78 / 100 · HIGH
RESPONSE PAYLOAD
· Score breakdown
topo 32 · pavement 21 · basin 18 · complaints 7
· LiDAR geometry
low-point depth, 2-in ponding volume, catchment polygon
· 311 history
3 flooding reports within 100 m since 2023
· APS cross-section
browser-viewable 3D profile — no CAD software needed
· Recommended action
clear upstream basin; do not resurface until drainage resolved
CurbRisk · Cyvl Hackathon 2026
6 / 7

## Slide 7
WHAT'S NEXT
From one Somerville tile to a city-wide risk layer.
NOW
Hackathon MVP
One Somerville tile end-to-end. Address → score + APS cross-section in < 10 s.
NEXT
Paid pilot
$20–50K fixed-scope study with a Somerville-style city. One paving package, one Autodesk model, one reference customer.
THEN
Insurer dataset
Bulk drainage-risk layer for one metro area, licensed to a cat modeler. Recurring revenue, no per-city sales cycle.
Stop pricing flood risk with a map that ends at the parcel.
Start pricing it with the one that ends at the curb.
CurbRisk · Cyvl Hackathon 2026
7 / 7